## Slide 1
This work builds and evaluates a low-cost educational IIoT platform combining an MCU (ESP32-S3), an SBC (Raspberry Pi 4), and a PLC (Siemens LOGO! 24CE). On the MCU, a Modbus RTU-to-TCP/MQTT gateway bridges legacy serial field devices to modern IT systems; eight open-source ESP32 gateway libraries are benchmarked on real hardware for latency, throughput, and flash/RAM use to select one. Open-source software — Mosquitto, the TIG stack, and Node-RED — carries the IT and edge layers, while a passive IoT-Sniffer decodes Modbus TCP and MQTT on the wire for direct protocol visibility. Results show a single sub-2,000-THB microcontroller bridges legacy OT to an IT dashboard within its firmware budget, and the three controller classes prove complementary, not competing, teaching roles.
Abstract
Objectives
Design and build a low-cost educational IIoT platform integrating three controller classes: SBC (Raspberry Pi 4), MCU (ESP32-S3), and PLC (Siemens LOGO! 24CE).
Demonstrate IT/OT integration on an open-source stack — MQTT broker (Mosquitto), Node-RED, and the TIG stack (Telegraf, InfluxDB, Grafana) — as the edge and IT layers.
Implement a Modbus RTU-to-TCP/MQTT gateway on the MCU; benchmark open-source ESP32-S3 Modbus libraries on real hardware and measure the chosen gateway's latency, throughput, and flash/RAM use.
Develop an IoT-Sniffer that decodes Modbus TCP and MQTT on the wire to observe and measure the platform's network performance.
Conclusion and Contribution
A single sub-2,000-THB microcontroller bridges legacy serial OT to an IT dashboard within its firmware budget (72% flash, 15% RAM). The MCU, SBC, and PLC prove complementary, not competing: the MCU suits the field-edge gateway, the SBC the data plane, and the PLC certified, deterministic control. Future work: add a telemetry ring buffer and OTA updates to the gateway; add InfluxDB backups, container health checks, and Grafana alerting to the IT layer; study OPC-UA for broader interoperability; and trial the platform with students in a laboratory course to assess its educational value before pursuing real deployment.
Acknowledgement
The author thanks the project advisor, examination committee, and the ECE Department, KMUTNB, for their guidance and support.
s6301011610279@email.kmutnb.ac.th
Department of Electrical and Computer Engineering, Faculty of Engineering
King Mongkut's University of Technology North Bangkok, Bangkok, Thailand
Introduction
Industry 4.0 pushes factories to expose shop-floor data to IT systems for monitoring and remote supervision, yet operational-technology (OT) equipment still speaks decades-old protocols. Modbus, introduced in 1979, remains one of the most widely deployed field protocols, and in its serial RTU form runs over RS-485 with no native path to an IP network. Replacing legacy field hardware outright is rarely economic, so the real problem is integration: lifting OT signals into IT dashboards at low cost without compromising the determinism OT depends on. Students entering the field must understand all three controller classes — MCU, SBC, and PLC — which differ not only in compute and I/O but in software ecosystem: the MCU and SBC run open-source toolchains (Arduino/PlatformIO, Linux/Docker), while the PLC is locked to a proprietary vendor toolchain. Commercial IIoT trainers are expensive and closed, hiding the wire-level behaviour learners need to see, and no empirical comparison guides which open-source Modbus library to use.
Patthanan Bhundhumani
Advisor: Dr.-Ing. Rawat Siriphokhapirom
Design and Implementation of an Educational Industrial IoT Platform Combining SBC, MCU, and PLC
Related Courses :
Course ID
010113027
010113029
Course Name
MICROPRO & EMBEDDED COMP SYS
COMPUTER PROGRAMMING
Copyright © Department of Electrical and Computer Engineering, King Mongkut's University of Technology North Bangkok, Bangkok, Thailand
Academic Year : 2025
Methodology
Overall architecture: the platform integrates the three controller classes on a single LAN. Field instruments — an XY-MD02 temperature/humidity sensor and an Eastron SDM230 power meter — are Modbus RTU slaves on an RS-485 bus. The Siemens LOGO! 24CE PLC performs deterministic control with industrial I/O; the ESP32-S3 edge gateway converts protocols; the Raspberry Pi 4 hosts the MQTT broker and the TIG data plane.
Two data paths run in parallel. Path A (direct Modbus TCP): any LAN host, including the PLC acting as master, polls a Modbus TCP server. Path B (telemetry pipeline): the ESP32-S3 polls the RTU sensors, publishes JSON over MQTT, and Telegraf ingests it into InfluxDB for display in Grafana.
Gateway timing budget (per cycle):
t(RTU poll) + t(MQTT publish) + t(TCP service) < 2,000 ms
The production firmware runs the chosen Modbus library as a TCP slave, a hand-rolled RTU master, an MQTT publisher, and a watchdog from one cooperative loop: 946 KB / 1,310 KB flash (72.2%) and 48.5 KB / 327.6 KB RAM (14.8%) — a complete dual-protocol gateway with headroom to spare.
Library selection: emelianov/modbus-esp8266 was chosen — the only actively maintained candidate offering RTU master, Modbus TCP slave, and multi-client TCP together (see Analysis and Results).
Concurrent firmware roles: each pass of the cooperative loop services a Modbus RTU master (polls the field sensors over RS-485 with CRC-16 framing, FC03/FC04), an MQTT publisher (serialises readings to JSON at QoS 1), a Modbus TCP slave (serves the same readings on port 502 as holding registers HR0–HR20), and a watchdog (forces a clean restart on a stalled cycle).
IoT-Sniffer: a passive Python protocol analyser verifies the gateway on the wire. It runs scapy's AsyncSniffer directly on the host NIC — no tap or port-mirror needed — and decodes Modbus TCP and MQTT at the application layer, reassembling out-of-order TCP segments and parsing the MBAP header and function codes to confirm every request/response pair matches firmware intent.
Analysis and Results
System architecture (below): the Raspberry Pi 4 (TIG stack + MQTT + IoT-Sniffer) bridges over Ethernet to a wired industrial network (PLC, Modbus TCP) and a wireless edge (ESP32-S3, MQTT + Modbus RTU master).
References
[1] S. Santos, P. Costa, and A. Rocha, "IT/OT convergence in Industry 4.0: risks and analysis of the problems," in Proc. 18th Iberian Conf. on Information Systems and Technologies (CISTI), 2023.
[2] L. D. Xu, E. L. Xu, and L. Li, "Industry 4.0: state of the art and future trends," Int. J. Prod. Res., vol. 56, no. 8, pp. 2941-2962, 2018.
[3] Enterprise-Control System Integration - Part 1: Models and Terminology, ISA-95.00.01, 2010.
[4] Modbus Organization, Modbus Application Protocol Specification V1.1b3, 2012.
[5] Information technology - Message Queuing Telemetry Transport (MQTT) v3.1.1, ISO/IEC 20922, 2016.
[6] InfluxData, "Telegraf 1.28 documentation," 2024. [Online]. Available: https://docs.influxdata.com/telegraf/.
[7] InfluxData, "InfluxDB 2.7 documentation," 2024. [Online]. Available: https://docs.influxdata.com/influxdb/v2/.
[8] Grafana Labs, "Grafana documentation," 2024. [Online]. Available: https://grafana.com/docs/grafana/latest/.
Table 1. FC03 round-trip latency, ESP32-S3, 100 registers, 9,600 baud (5 of 8 libraries benchmarked).
Library | Mean (ms) | Flash (KB) | RAM (KB) | Note
tobiasfaust (RTU) | 27.7 | 300 | 22.0 | Fastest
espressif/esp-modbus | 28.0 | 270 | 14.4 | Smallest RAM
eModbus/eModbus | 30.3 | 384 | 22.9 | FreeRTOS alt.
zivillian/eModbus | 32.9 | 384 | 22.9 | 132 ms outlier
emelianov/modbus-esp8266 | 33.4 | 310 | 22.2 | Recommended
All 8 libraries passed the stress suite; every candidate sits within ~10 ms of the ~24 ms wire-time floor, well under the platform's 2-second telemetry cycle.
Built as a complete gateway — Modbus TCP slave, RTU master, MQTT publisher, and watchdog in one cooperative loop — the production firmware occupies 946 KB of the 1,310 KB app partition (72.2%) and 48.5 KB of 327.6 KB RAM (14.8%). End to end, an RTU poll, register update, MQTT publish, and TCP slave service complete well inside the two-second cycle, confirming a complete dual-protocol gateway fits a low-cost MCU with headroom to spare.