## Slide 1
ESP32 Modbus Library Evaluation
Multi-environment PlatformIO sweep on ESP32-S3 DUT vs ESP32-C6 mock slave
Patthanan Bhandhumanee
2026-05-14
Survey reference: modbus_lib_eval_2026-05-11.pdf · 10 candidate projects

## Slide 2
Goal & Scope
What does this experiment answer?
• Take 10 ESP32 Modbus projects from the PDF survey rubric and put each one on real hardware.
• ESP32-S3 is the device under test (DUT). It is flashed with one candidate library at a time.
• ESP32-C6 is a small custom Modbus RTU slave fixture (the same mock slave for every DUT).
• Each DUT exercises a fixed FC3 / FC6 / FC16 cycle against the C6 and prints PASS / FAIL per step.
• Output: a per-candidate verdict on framework compatibility, flash & RAM usage, and runtime behavior.
• Style constraint: each DUT sketch is plain Arduino-IDE-style code — setup() / loop() / free helpers — no project-level OOP or shared harness.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
2 / 15

## Slide 3
Hardware setup
Two boards over RS485
ESP32-S3 (DUT)
4D Systems Gen4 R8N16
UART1 TX = GPIO 9
UART1 RX = GPIO 8
9600 8N1
RS485 bus (auto-direction transceiver)
A ↔ A · B ↔ B · GND ↔ GND
ESP32-C6 (mock slave)
DevKitC-1
UART1 TX = GPIO 4
UART1 RX = GPIO 5
Slave ID = 1
C6 holding registers (initial values): [100, 200, 300, 400, 500, 600, 700, 800, 900, 1000]
Function codes supported by C6: FC03 read holding, FC06 write single, FC16 write multiple, plus standard exception responses.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
3 / 15

## Slide 4
Test cycle (same for every DUT)
Four steps, repeated forever with a 3 s pause
Step | Function code | What the DUT does | Pass condition
T1 | FC03 read | Read holding regs 0..4 | Values are 100, 200, 300, 400, 500
T2 | FC06 write | Write reg 0 = 4242 | Slave echoes the write frame
T3 | FC03 read | Read reg 0 again (verify T2) | Value is 4242
T4 | FC16 write | Write regs 0..2 = 100, 200, 300 (restore) | Slave acks; state is back to baseline
Each cycle ends with a serial line: "CYCLE SUMMARY: n/m PASS". Counters are global to that DUT firmware.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
4 / 15

## Slide 5
10 candidates · per-project strategy
How each library was actually exercised
# | Candidate | Framework | Strategy
1 | Rob2011/ESP32.Modbus-TCP-gateway | Arduino | Use emelianov/modbus-esp8266 ModbusRTU master directly.
2 | vwetter/esp32-modbus-gateway | Arduino | vwetter has no Modbus library; DUT mirrors its raw HardwareSerial RTU.
3 | zivillian/esp32-modbus-gateway | Arduino | Upstream PIO fails on Arduino core 3 (HTTP_GET clash); DUT uses the eModbus layer their gateway wraps.
4 | harihanv/esp32-modbus-gateway | Arduino | ArduinoRS485 1.1.1 is unusable on ESP32; DUT uses raw RTU like harihanv's own code.
5 | tobiasfaust/SolaxModbusGateway | Arduino | Solax modbus class is tied to LittleFS/MQTT/inverter; DUT mirrors their RS485 test sketch.
6 | eModbus/eModbus | Arduino | Direct use of ModbusClientRTU, modeled on the upstream RTU04 example.
7 | NamNamIoT/ESP32 | Arduino | Their Modbus_RTU.ino uses 4-20ma/ModbusMaster; DUT mirrors it on Serial1.
8 | maxx-ukoo/esp32-modbus-tcp2rtu | ESP-IDF | Full TCP↔RTU gateway needs SPIFFS / MQTT / WiFi. DUT runs the same esp-modbus path their modbus.c uses.
9 | espressif/esp-modbus | ESP-IDF | Minimal app_main using mbc_master_send_request (FC3/FC6/FC16).
10 | rosenrot00/esphome_modbus_bridge | ESPHome | Excluded from PlatformIO — ESPHome is its own toolchain; evaluate separately.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
5 / 15

## Slide 6
PlatformIO environments
1 fixture + 7 Arduino DUTs + 2 ESP-IDF DUTs = 10 envs
Env | Framework | Source | Library
esp32-c6-fixture | arduino | src/ESP32C6/main.cpp | raw RTU slave
dut_rob2011_arduino_s3 | arduino | src/dut/rob2011/main.cpp | emelianov ModbusRTU
dut_vwetter_arduino_s3 | arduino | src/dut/vwetter/main.cpp | raw HardwareSerial
dut_zivillian_arduino_s3 | arduino | src/dut/zivillian/main.cpp | eModbus ModbusClientRTU
dut_harihanv_arduino_s3 | arduino | src/dut/harihanv/main.cpp | raw HardwareSerial
dut_tobiasfaust_arduino_s3 | arduino | src/dut/tobiasfaust/main.cpp | raw HardwareSerial
dut_emodbus_arduino_s3 | arduino | src/dut/emodbus/main.cpp | eModbus (direct)
dut_namnam_iot_arduino_s3 | arduino | src/dut/namnam_iot/main.cpp | 4-20ma/ModbusMaster
dut_esp_modbus_espidf_s3 | espidf | src/dut/esp_modbus/main.c | esp-modbus master
dut_maxx_ukoo_espidf_s3 | espidf | src/dut/maxx_ukoo/main.c | esp-modbus (same lib)
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
6 / 15

## Slide 7
Build results
10/10 environments produce a flashable firmware
Env | Status | Flash (B) | Flash % | RAM (B) | RAM % | Build time
esp32-c6-fixture | SUCCESS | 252,882 | 19.3% | 13,852 | 4.2% | ≈ 8 s
dut_rob2011_arduino_s3 | SUCCESS | 310,437 | 9.9% | 22,156 | 6.8% | ≈ 9 s
dut_vwetter_arduino_s3 | SUCCESS | 300,501 | 9.6% | 21,996 | 6.7% | ≈ 8 s
dut_zivillian_arduino_s3 | SUCCESS | 384,105 | 12.2% | 22,932 | 7.0% | ≈ 14 s
dut_harihanv_arduino_s3 | SUCCESS | 300,213 | 9.5% | 21,996 | 6.7% | ≈ 8 s
dut_tobiasfaust_arduino_s3 | SUCCESS | 300,157 | 9.5% | 21,996 | 6.7% | ≈ 8 s
dut_emodbus_arduino_s3 | SUCCESS | 384,033 | 12.2% | 22,940 | 7.0% | ≈ 12 s
dut_namnam_iot_arduino_s3 | SUCCESS | 301,573 | 9.6% | 22,292 | 6.8% | ≈ 8 s
dut_esp_modbus_espidf_s3 | SUCCESS* | 269,553 | 1.6% | 14,448 | 4.4% | ≈ 49 s
dut_maxx_ukoo_espidf_s3 | SUCCESS* | 269,517 | 1.6% | 14,448 | 4.4% | ≈ 49 s
* ESP-IDF envs built from /tmp/modbus_eval_real to dodge the project-path whitespace bug.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
7 / 15

## Slide 8
Resource usage — three clear groups
Why the numbers cluster the way they do
Raw HardwareSerial (~300 KB)
• vwetter, harihanv, tobiasfaust
• No Modbus library at all
• Just Arduino baseline + tiny RTU helpers
• ≈ 21 996 B RAM, ≈ 300 KB flash
• Honest representation of these candidates
Middleweight master libs
• rob2011 (emelianov), NamNamIoT (4-20ma ModbusMaster)
• ≈ 22 200 B RAM, ≈ 310 KB flash
• Synchronous APIs, small footprint
• About 10 KB above the Arduino baseline
Async / Pro stacks
• zivillian, eModbus (both ModbusClientRTU)
• ≈ 22 900 B RAM, ≈ 384 KB flash
• Background FreeRTOS worker task
• +84 KB over baseline for async + queues
• ESP-IDF envs use ≈ 270 KB / 14 KB — lighter startup than Arduino-on-IDF
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
8 / 15

## Slide 9
Excluded / known issues
Honest evaluation per PDF criteria
• rosenrot00/esphome_modbus_bridge — ESPHome only; not a PlatformIO framework. Evaluate with `esphome compile` against the same C6 fixture.
• harihanv/esp32-modbus-gateway — Upstream ArduinoRS485 1.1.1 expects SERIAL_PORT_HARDWARE / A5 / A6; will not compile on ESP32-S3. DUT falls back to raw HardwareSerial, which is what the gateway itself uses.
• zivillian/esp32-modbus-gateway — Upstream PIO project fails on Arduino core 3.x: HTTP_GET / HTTP_POST symbol clash between ESPAsyncWebServer fork and ESP-IDF http_parser. DUT exercises the eModbus layer their gateway sits on.
• tobiasfaust/SolaxModbusGateway — `modbus` class is tied to LittleFS config, MQTT, and Solax inverter registers; not a reusable Arduino library. DUT mirrors their RS485 example.
• maxx-ukoo/esp32-modbus-tcp2rtu — Full gateway needs an npm-built web SPIFFS, MQTT broker, and station-mode WiFi. Out of scope for an RS485-only rig. DUT runs the same esp-modbus path their modbus.c wraps.
• pioarduino espidf builder bug — Unquoted `-fmacro-prefix-map=$PROJECT_DIR=.`; current project path has a space ("Senior Project"). Workaround: rsync the project to a no-space path before building the two ESP-IDF envs.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
9 / 15

## Slide 10
Repo layout
Where to find each piece
ESP32_c6_s3_modbus/ # PIO project root (git)
├── README.md # entry doc: hardware, envs, results, flash plan
├── platformio.ini # 10 environments
├── CMakeLists.txt # ESP-IDF project root (used only by espidf envs)
├── docs/ # generated outputs
│ ├── modbus_lib_eval_2026-05-11.pdf # source survey rubric
│ ├── modbus_lib_eval_report.docx # full hardware test report
│ ├── modbus_lib_eval_presentation.pptx # this deck
│ └── evaluation_template.xlsx # rubric + Build Results (PIO 2026-05-13) sheet
├── src/
│ ├── ESP32C6/main.cpp # mock RTU slave fixture
│ ├── ESP32S3/main.cpp # baseline raw-RTU master
│ ├── CMakeLists.txt # IDF main component
│ └── dut/{rob2011, vwetter, zivillian, harihanv, tobiasfaust,
│ emodbus, namnam_iot, esp_modbus, maxx_ukoo}/main.{cpp,c}
└── lib/ # 10 upstream candidate libraries
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
10 / 15

## Slide 11
How to reproduce
PlatformIO Core 6.1.19 · pioarduino 55.3.38 · ESP-IDF 5.5.4
1. Build all eight Arduino envs from the project root:
pio run -e esp32-c6-fixture -e dut_rob2011_arduino_s3 \
-e dut_vwetter_arduino_s3 -e dut_zivillian_arduino_s3 \
-e dut_harihanv_arduino_s3 -e dut_tobiasfaust_arduino_s3 \
-e dut_emodbus_arduino_s3 -e dut_namnam_iot_arduino_s3
2. Build the two ESP-IDF envs from a no-space path:
rsync -a --delete --exclude='.pio' --exclude='.git' \
<project> /tmp/modbus_eval_real/
cd /tmp/modbus_eval_real
pio run -e dut_esp_modbus_espidf_s3 -e dut_maxx_ukoo_espidf_s3
3. Flash the C6 fixture once, then flash each DUT env in turn and monitor:
pio run -e esp32-c6-fixture --target upload
pio run -e <dut_env> --target upload && pio device monitor -e <dut_env>
4. Watch the serial monitor for "CYCLE SUMMARY: 4/4 PASS" per cycle.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
11 / 15

## Slide 12
Hardware test — PASS / FAIL
9 DUT envs · C6 mock slave · 2026-05-14
C6 fixture flashed once; each S3 DUT flashed in turn; 18 s serial capture each; 188 / 188 step results PASS across 47 cycles.
Env | Runtime | Library exercised
dut_rob2011_arduino_s3 | PASS 20/20 | emelianov ModbusRTU sync
dut_vwetter_arduino_s3 | PASS 20/20 | raw RTU on HardwareSerial
dut_zivillian_arduino_s3 | PASS 20/20 | eModbus ModbusClientRTU
dut_harihanv_arduino_s3 | PASS 24/24 | raw RTU (ArduinoRS485 unusable on ESP32)
dut_tobiasfaust_arduino_s3 | PASS 20/20 | raw RTU (Solax lib not reusable)
dut_emodbus_arduino_s3 | PASS 20/20 | eModbus ModbusClientRTU
dut_namnam_iot_arduino_s3 | PASS 20/20 | 4-20ma ModbusMaster
dut_esp_modbus_espidf_s3 | PASS 24/24 | esp-modbus mbc_master_send_request
dut_maxx_ukoo_espidf_s3 | PASS 24/24 | esp-modbus (path their gateway wraps)
Every DUT exercised FC3 read · FC6 write · FC3 verify · FC16 restore with zero failed steps.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
12 / 15

## Slide 13
Round-trip latency
micros() / esp_timer_get_time() · 9600 8N1 · 31-32 samples/env
Wire-time floor @ 9600 8N1: FC3-1reg 19.3 ms · FC6 20.3 ms · FC16 26.6 ms · FC3-5regs 27.6 ms.
Env | N | min | mean | p50 | p95 | max
rob2011 (emelianov sync) | 31 | 27.97 | 33.39 | 29.97 | 39.97 | 39.97
vwetter (raw RTU) | 31 | 22.16 | 27.90 | 24.16 | 34.16 | 34.16
zivillian (eModbus async) | 32 | 24.00 | 32.88 | 28.99 | 36.00 | 132.34*
harihanv (raw RTU) | 31 | 22.18 | 28.01 | 24.18 | 34.18 | 34.18
tobiasfaust (raw RTU) | 31 | 22.15 | 27.73 | 24.16 | 34.16 | 34.16
emodbus (eModbus async) | 31 | 24.00 | 30.25 | 26.00 | 36.00 | 36.00
namnam_iot (ModbusMaster) | 31 | 19.16 | 24.45 | 20.79 | 30.62 | 30.75
esp_modbus (IDF) | 32 | 22.28 | 27.97 | 27.54 | 34.14 | 34.27
maxx_ukoo (IDF) | 32 | 22.34 | 27.82 | 27.29 | 34.40 | 34.53
All numbers in ms across all 4 steps. *zivillian: one 132 ms first-cycle outlier (eModbus worker spin-up); steady-state matches emodbus.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
13 / 15

## Slide 14
Latency observations
Why each library lands where it does
• namnam_iot (4-20ma ModbusMaster) is wire-speed: 19.16 ms minimum on FC3-1reg matches the 19.3 ms theoretical floor. No extra polling, no quantization.
• Raw-RTU sketches (vwetter, harihanv, tobiasfaust) cluster ~3 ms above wire-time. The 4 ms FRAME_GAP_MS silence detector accounts for the overhead.
• ESP-IDF esp-modbus (esp_modbus, maxx_ukoo) matches raw-RTU within noise (22-34 ms). Official Espressif library runs at wire-speed despite a separate FreeRTOS controller task.
• eModbus envs (emodbus, zivillian) add ~2 ms per step from the 2 ms delay(2) result poll. All completions quantize to even-ms boundaries (24/26/36 ms).
• rob2011 (emelianov sync) is the slowest, ~6-8 ms over wire-time. mb.task() polls in 2 ms ticks with an extra 1 ms internal quantum, giving the clean 28/30/36/40 ms steps.
• Single 132 ms outlier on zivillian first cycle = eModbus worker task scheduling delay right after begin(). Subsequent cycles match emodbus exactly.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
14 / 15

## Slide 15
Conclusion & future work
What we learned · what comes next
Outcomes
• Nine of ten candidates from the PDF rubric evaluated end-to-end on real hardware through PlatformIO.
• Framework-compatibility verdicts concrete: ESP-IDF (esp-modbus, maxx-ukoo), Arduino-ESP32 (the rest), ESPHome-only (rosenrot00).
• Resource numbers separate into three groups: raw-RTU baseline, middleweight master libs, async/eModbus stacks.
• All 9 DUTs pass 188/188 functional steps; round-trip latency measured 19-40 ms covering wire-speed, raw, eModbus-async, and emelianov-sync regimes.
• Upstream build blockers identified: zivillian HTTP_GET, harihanv ArduinoRS485 — both documented with working replacements.
Future work
• Automated serial-port harness scraping CYCLE SUMMARY + [us=N] into the XLSX.
• Run rosenrot00 ESPHome candidate via esphome compile against the same C6 fixture.
• Extend cycle to FC01/FC02/FC04/FC05/FC15 plus exception responses.
• Higher baud rate sweep (19200, 38400, 115200) to separate library overhead from wire-time.
ESP32 Modbus Library Evaluation · Patthanan Bhandhumanee · 2026-05-14
15 / 15